## Slide 1: Printed Circuit Board Design on AutoDesk Eagle
By: Sriram Boppana
How to think[Box]!

## Slide 2: Before we begin
Follow this link and download the repository:
  https://github.com/boppana113/Workshops
  Unzip the .zip file
  Open the powerpoint for this workshop
Download AutoDesk Eagle if you have not already:
https://www.autodesk.com/products/eagle/free-download
If you do not have a computer, please let us know so we can provide you a computer with Eagle installed already

## Slide 3: Agenda
What is a Printed Circuit Board?
Intro to AutoDesk Eagle
Design an Accelerometer Breakout board
  Schematic Layout
  Board Layout
Order your PCB?
Where can I learn more?

## Slide 4: What is a Printed Circuit Board (PCB)?
PCBs mechanically support and connects electronic components together that are connected using conductive and insulated materials.
Found in virtually all modern electronics from computers, mobile devices, and other gadgets

## Slide 5: What is a Printed Circuit Board (PCB)?
Photo from www.sparkfun.com
Photo from hephaestusaudio.com

## Slide 6: PCB Layers: 1, 2 or more?

## Slide 7: EAGLE: A CAD Tool for Designing a Board
Schematic
Layout
Board
Layout
Control Panel
Project
Add your components
Connect Everything together

## Slide 8: Schematic and Board Layout
Schematic Layout
Board Layout
PCB

## Slide 9: Symbol + Footprint + Device = Component
Device
Dev
Symbol
Sym
Footprint
Pac
Schematic Capture
Layout

## Slide 10: Example PCB Design: IntelliSleeve

## Slide 11: Schematic: IntelliSleeve

## Slide 12: Example PCB Design: NRF52 SoC with Bluetooth Antenna Breakout

## Slide 13: Stuff I need to get started
A Plan
  Component Selection
  Connections and Testing Considerations
  Power and Performance Considerations
A New Project
Access to the library and components you need

## Slide 14: Design an Accelerometer Breakout
For this workshop, you will design an ADXL345 accelerometer breakout board.
  3 axis accelerometer
  https://www.sparkfun.com/products/9836

## Slide 15: How does an accelerometer work?

## Slide 16: How does ADXL 345 send acceleration data?
ADXL organizes the data using the I2C communication protocol
  https://learn.sparkfun.com/tutorials/i2c
The Arduino decodes the data from I2C which the user can read

## Slide 17: Add Libraries to Eagle
In the control panel, click on options > directories
In the new window, click on libraries, then click browse
In the extracted zip file from slide 2, click on the folder labelled “libraries” under workshops-master->eagle
Figure obtained from Sparkfun.com

## Slide 18: Component Terminology
DIP
LQFP, QFP, TQFP
QFN
BGA
Thru-Hole (TH)
Surface Mount (SMT)
Resistor
Capacitor
SMT Resistor and Capacitor Sizes

## Slide 19: Creating a Schematic
Launch Eagle
File -> New -> Project
Enter Project Name: “myfirstPCB”
Active project is shown with a green light.
Right Click Project -> New Schematic

## Slide 20: ADXL 345: Reference Schematic
Accelerometer
Connector
Bypass capacitors

## Slide 21: Add ADXL 345

## Slide 22: Add 8-pin connectors

## Slide 23: Add 0.1uF capacitor (x2)

## Slide 24: Board Layers

## Slide 25: Design Rule Check

## Slide 26: ADXL 345: Reference Board Layout
ADXL 345
Connectors
Capacitors

## Slide 27: Order your PCB!
Oshpark: https://oshpark.com/
  Standard service
    $5/in^2 with three board copies – 2 weeks fabrication
  Super-swift service
    10/in^2 with three boards – 3 day fabrication
Thinkbox: http://thinkbox.case.edu/equipment/pcbrouter

## Slide 28: General Advice
Design your board twice, print it once!
  Mistakes on your PCB can cost you precious time to fix.
  Making a board design more than once reduces the number of errors made and increases your efficiency at designing the board.
Recheck the design rules
  Typically 8mils of clearance is ok (1mil = 1/1000th of an inch)
Place Components
Route Traces
Fab!
Iteration
Generate Gerbers
Schematic Capture

## Slide 29: Where can I learn more?
Autodesk eagle:
  http://eagle.autodesk.com/eagle/documentation
Sparkfun:
  https://www.sparkfun.com/EAGLE